## Slide 1: BURT at DLS
Will Rogers
Controls Group

## Slide 2: Background
One big accelerator
  Plus linac and booster synchrotron
Fixed lattice – changes every year or so
Different ‘optics’ – operation modes

## Slide 3: BURT
Back-up and restore tool
Just snapshots of PV values
Restores the machine to a known state
Switches the machine between operational modes
After ‘burting’, AP use the LOCO algorithm to fine-tune the configuration

## Slide 4: Burt implementation
Old-school EPICS extension
Written in C
22 files, 8000 lines of code
Not (really) updated since 2008

## Slide 5: Burt implementation
Extension developed at DLS (circa 2010?) to group multiple snapshot files
Python-Qt gui developed to manage the files
Post to elog when saving and restoring

## Slide 6: Burt at DLS
Current usage defined by experience
250 ‘request’ files
60k ‘snapshot’ files (!)
Not well versioned

## Slide 7: Possible improvements
‘Check’ files:
  Raise a warning if a PV value does not match its expected value
‘Write-only’ values:
  The value at the time of the snapshot is less important than the ‘correct’ value

## Slide 8: Overall
Pros:
  Simple
  Stable
  Reliable
Cons:
  File management is a little tricky
  Further development would be tricky

## Slide 9: Beamlines
Burt is not widely used
Defaults are set at IOC build time
Autosave restore:
  Reset PVs to sensible values on IOC restart

## Slide 10: Masar
Machine Snapshot, Archiving and Retrieval
Very much like Burt in principle

## Slide 11: Masar
Developed by Guobao Shen at NSLS-II
Relational database storage
?C++ implementation?
?Java application server (Wildfly)?
Plotting, compare tools
EPICS v4 API
Scriptable with Python

## Slide 12: Score?
Save compare restore
Associated with OpenXAL project
Details are difficult to come by

## Slide 13: Discussion…